## Slide 1: EE 690: Interconnection Network for HPC Systems Introduction to YACSIM/NETSIM
Avinash Karanth
Department of Electrical Engineering & Computer Science
Ohio University, Athens, Ohio 45701
E-mail: karanth@ohio.edu
Website: http://ace.cs.ohio.edu/~avinashk/classes/ee690/ee690.htm

## Slide 2
YACSIM: Discrete-event Simulator
YACSIM is a discrete-event simulation language based on C
programming language
YACSIM extensions to C are organized as a set of simulation objects
3 categories of objects: activities, queues and statistics records
Activities: active components of a simulation, account for passage of
time, modify the state of a simulation
Queues: Synchronization and model resources
Statistics Records: Collection, presentation of information
generated by simulation

## Slide 3
Activities, Queues and Statistics
Records
Processes & Events: Activity of a simulated system
Event-driven: the only way to advance time is to schedule an
event to occur at some time in the future
Process-driven: the processes can account for the passage
of time by delaying themselves [Does not work in Cygwin]
Queues for synchronization: semaphores, barriers, flags and
conditions
Resources for modeling queues and servers, request service,
queuing discipline, etc
Statistics Records: collect mean, standard deviation, etc

## Slide 4
Activities (1/3)
Main difference between Process and Events: body of a
process maybe temporarily suspended, while the body of
an event cannot.
When an event is rescheduled, it will start from the beginning
of the body
Processes can have a lifetime that extends over a period
of simulation time, where as events occur at one instant in
simulation time
Do not use processes if running the code in Cygwin

## Slide 5
Schedule an activity to happen:
- after a given time
- when a given semaphore value is positive
- when a given flag is set
- when a given condition holds, or
- after a requested amount of service from a resource
Schedule an activity from any part of the program that has access to the
activity, i.e. within the body of a process/event
- Scheduling process may suspend
- Link the scheduled activity with other activities
- Schedule an independent activity
Processes terminate when their bodies terminate, suspension is not
termination
Activities (2/3)

## Slide 6
Scheduling Operations:
void ActivitySchedTime(aptr, timeinc, blkflg)
- aptr = argument that points to the activity (ACTIVITY *aptr)
- timeinc = when should the scheduling start (double )
- blkflg = INDEPENDENT, BLOCK, FORK (int )
void ActivitySchedSema(aptr, semptr, blkflg)
ACTIVITY *ActivityArgSize(aptr)
- returns the size of the argument passed
Activities (3/3)

## Slide 7
PROCESS *NewProcess(pname, bodyname, stksz)
void ProcessDelay(timeinc)
void ProcessSleep()
- Should make some other activity to schedule the sleeping
process
ProcessSendMsg(dest, buf, bytes, blkflg, type)
ProcessReceiveMsg(buf, bytes, blkflg, type, sender)
ProcessCheckMsg(type, sender)
Processes

## Slide 8
EVENT *NewEvent(ename, bodyname, delflg, etype)
void EventSetDelFlag()
void EventReschedTime(timeinc, stval)
void EventReschedSema(semptr, stval)
int EventSetState(stval)
int EventGetState()
Events

## Slide 9
SEMAPHORE *NewSemaphore(sname, i)
void SemaphoreSignal(sptr)
void SemaphoreSet(sptr)
void SemaphoreWait(sptr)
void SemaphoreDecr(sptr)
int SemaphoreValue(sptr)
int SemaphoreWaiting(sptr)
Semaphores

## Slide 10
Simulation Driver
int DriverRun(timeinc)
- This operation starts or restarts the simulation. Once, the
user invokes this operation, the simulator will run for
timeinc units of simulation, until the event list is empty.
- If timeinc = 0.0, the simulator will run until the event list is
empty

## Slide 11
NETSIM: A Network Simulation Library
NETSIM can be used to construct and simulate a wide range
of network models, including direct and indirect networks
Interconnection networks are usually constructed from
switches and links
Switch is a device with one or more input terminals that can
route data selectively from input terminals to output terminals
Links are communication channels used to connect switch
output terminals to input terminals of other switches

## Slide 12
Routing protocol is mechanism for controlling the movement
of data through switches and links
Data is mostly organized into packets consisting of several
smaller units of data called flits
Flit is the smallest unit of data that can be transferred
between two switches in a single cycle
The first flit, called the head flit of a packet contains the
routing information used by the switches to select output
terminals
The last flit is called the tail, it tears the path
NETSIM

## Slide 13
NETSIM Modules
Multiplexers: Multiple input, single output modules. Resolves
conflict when two of its input terminals have data to transfer
to the same output terminal
Demultiplexers: Single input, mulitple output modules. Routes
data along several paths, uses the head flit for determining
routing information
Buffers: Temporary storage for flits (not packets) as they
move through the network, implemented as FIFO queues
Network Ports: Single input, single output modules, interface
between a network and its external environment, Input Port
and Output Port, holds an entire packet

## Slide 14
NETSIM Implementation
Data is sent through the network in the form of packets
consisting of several flits
Each packet contains routing information used by demultiplexer
to route packets through the network
Each packet is implemented as 2 YACSIM events, one for
the front end or head of the packet and one for the rear or tail
of the packet
Head sets up the path, tail tears up the path

## Slide 15
NETSIM Operations
BUFFER *NewBuffer(id, size)
MUX *NewMux(id, fanin)
DEMUX *NewDemux(id, fanout, routingfcn)
- Arguments for routing function (src, dest, id)
IPORT *NewIPort(id, size)
OPORT *NewOPort(id, size)
void NetworkConnect(src, dest, src_index, dest_index)
- src_index used by demultiplexer to next module
- dest_index used by multiplexer to next module

## Slide 16
Network Delays
void NetworkSetCycleTime(x) – System cycle time
void NetworkSetFlitDelay(d) – From buffer to buffer or port
void NetworkSetMuxDelay(d) – Mux switching delay
void NetworkSetDemuxDelay(d) – Execute the routing fn
void NetworkSetPktDelay(d) – Time to move a packet into
an input port or output port

## Slide 17
Packet Operations
PACKET *NewPacket(seqno, msgptr, size, src, dest)
double PacketSend(pkt,port,src,dest)
PACKET *PacketReceive(port)
PKTDATA *PacketGetData(pkt)
void PacketFree(pkt)

## Slide 18
Packet Synchronization Operations
SEMAPHORE *IPortSemaphore(port)
int IportSpace(port)
SEMAPHORE *OportSemaphore(port)
int OportPackets(port)
int IportGetId(port)
int OportGetId(port)

## Slide 19
Network Statistics
NETTIME: time a packet spends in a network, packet latency
BLKTIME: time blocked in the network
OPORTTIME: time spent in oport
MOVETIME = NETTIME – BLKTIME
CREATETIME: time packet was created
void NetworkStatRept()
- Network throughput
- Average latency, etc

## Slide 20
Simple Example: Switch
IPort
Mux
Demux
IPort
OPort
OPort
Buffer
Buffer